## Slide 1: MAE 5419: Low Thrust LEO to GEO Problem
By: Devin Quach

## Slide 2: The Goal:
Low Earth Orbit to Geosynchronous Orbit within a Time of Flight
  Min Fuel
    Obj. Function = Int(|T|)dt
  Two-Point Boundary Problem
    States: [Radial Distance, Radial Velocity, Horizontal Velocity]
    Controls: [Magnitude of Thrust , Angle of Thrust]
Notes: To min fuel means minimizing T
  Obj. Func.
  Min Energy – T^2
2 Pt Boundary Problem
  Specified Initial and Final states and time
  Controls
    Phi=0 Positioned to Thrust in orbit, Phi = 90 Thrust outward, Phi = -90 Thrust inward

## Slide 3: Calculus of Variations:
  Hamiltonian & Necessary Conditions
    Third necessary condition:
      Pontrayagin Minimum Principle to Find Thrust since Thrust is linear in H
  Method to Numerically Solve: Variation of Extremals or Steepest Descent

## Slide 4: Process of Variation of Extremals:
Guess Initial costates
Perturbating reduced differential equations and controls
Perturbating new states & costates using forward integration
Influence functions: perturbating new Initial costates
Modified to just Px since tf is specified

## Slide 5: Results:

## Slide 6: Debugging/Troubleshooting:
Bootstrap Method:
Initial guess for costates from a simpler version of the problem
Correlation btwn TOF, mdot, and mo
Mdot was small to make mo seem constant
Single Interval for Thrust
Optimal control not unique or non-existent
Remedied to be zero
Tau weighting did not influence much
Did not converge
Influence Matrix becomes NaN

## Slide 7: Areas of Improvements: Fixing Influence Function
Creating a Steepest Descent Model
Compare
Modify for free TOF
Adding another boundary condition